## Slide 1: Visualization in Smart Manufacturing
Dong SUN
The Hong Kong University of Science and Technology

## Slide 2: Introduction
Visualization in Smart Manufacturing
Sequence Synopsis: Optimize Visual Summary of Temporal Event Data
HKUST
ViDX: Visual Diagnostics of Assembly Line Performance in Smart Factories
Notes: This is the outline of the presentation.
First, I will introduce the background and motivation of visualization in Industry 4.0.
Then, I will present a taxonomy based on challenges in Industry 4.0 and the lifecycle of manufacturing.
After that, I will illustrate the four categories given by the taxonomy, namely, planning and scheduling visualization, manufacturing simulation visualization, manufacturing process visualization, and supply chain visualization.
Finally, I will conclude the work and make suggestions on directions of future research.

## Slide 3: Industrial Revolution
Introduction
The Rise of Industrial Big Data
What is “Smart”?
Potential Application Scenarios
HKUST
Notes: First, let me introduce you the background and motivation of visualization in Industry 4.0.

## Slide 4: Industrial Revolution
Introduction
HKUST
1800
1900
2000
Industrial revolution
1.
In 1784, the first loom was created.
Industrial revolution
2.
In 1870, the first conveyor belt was created at the Cincinnati Slaughterhouse.
Industrial revolution
3.
In 1969, the first programmable logic controller (PLC) , Modicon 084, was created.
1.
2.
3.
Industrial revolution
4.
now
The implementation of the physical information system.
1st industrial revolution
2nd industrial revolution
3rd industrial revolution
4th industrial revolution
Industry 4.0
The people, devices and systems in the value chain are connected.
All the related information is accessible in real time.
The components in the value chain are continuous optimized to meet personalized requirements.
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 5: The Rise of Industrial Big Data
Introduction
HKUST
Industry 4.0 (Germany), Industrial Internet (America), and Made in China 2025 (China): Emphasize the use of big data. Big data is an important feature in future.
The main factors for the rise of big data in the industrial field:
The vast amount of data generated in the manufacturing process are not fully dug.
The development of sensing and communication equipment makes it cheap to access real-time data.
Cloud computing provides computing power for big data processing.
Human experience and analysis cannot satisfy the requirement of the complex management.
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 6: What is “Smart”?
Introduction
HKUST
Artificial intelligence: Simulate and extend human intelligence through computer programs. It summarizes patterns from phenomena and provides tools for people.
Go master
Super doctors
Smart eyes
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 7: Potential Application Scenarios
Introduction
HKUST
Interactive and intelligent data analysis tools
Enterprise-level central database
Reporting tools
Analysis decision tools
devices
manufacturing
management
Domain expert
知识
(人)
Problem
model
data
?
Data scientist
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 8: Opportunities and Challenges
Visualization in Smart Manufacturing
Research Taxonomy
Planning and Scheduling Visualization
Manufacturing Simulation Visualization
HKUST
Supply Chain Visualization
Manufacturing Process Visualization
Conclusion and Future work
Notes: First, let me introduce you the background and motivation of visualization in Industry 4.0.

## Slide 9: Opportunities and Challenges
Visualization in Smart Manufacturing
HKUST
Manufacturing data are collected and network-accessible.
Traditional: table data, tedious, inefficient.
(Post et al., 2017)
Journal of Computing and Information Science in Engineering
Visualization: intuitive, easy, effective.
Visualization helps analyze manufacturing data.
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 10: Opportunities and Challenges
Visualization in Smart Manufacturing
HKUST
Difficulty in understanding, analyzing, and optimizing product manufacturing.
1. complex systems
2. sheer number of data
3. professional knowledge required
4. advanced algorithms
decode the complex system
bridge the gap between humans and data
do not require expertise
explain the algorithm result
Visualization
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 11: Research Taxonomy
Visualization in Smart Manufacturing
HKUST
The taxonomy is based on:
1. The challenges and opportunities brought about by Industry 4.0
The changeability and various constraints of planning and scheduling.
Vast simulation runs and complex manufacturing systems.
Complicated state info and unpredicted risks in production processes.
The globalization, hierarchy, and uncertainty of supply chains.
2. The lifecycle of product manufacturing
simulation
plan
production
supply
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 12: Research Taxonomy
Visualization in Smart Manufacturing
HKUST
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 13: Planning and Scheduling Visualization
Visualization in Smart Manufacturing
HKUST
How to explore and optimize product planning under certain constraints?
Constraints
Machine load
Equipment capacity
Bar chart-based visualization
Visually adjust the plan
(Wu, 2001) Information Visualization
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 14: Planning and Scheduling Visualization
Visualization in Smart Manufacturing
HKUST
How to explore and optimize product planning under certain constraints?
Pros:
Intuitive and effective
User friendly
Reveals bottlenecks
Cons:
Other constraints?
Coarse-grained
(Wu, 2001) Information Visualization
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 15: Planning and Scheduling Visualization
Visualization in Smart Manufacturing
HKUST
How to alleviate visual clutter and reveal frequent sequences in scheduling?
Severe visual clutter in the Gantt chart.
Adopt reordering and aggregation algorithms to reveal highly concurrent scheduling.
Visualization: the extended Gantt chart.
LiveGantt (Jo et al., 2014) TVCG
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 16: Planning and Scheduling Visualization
Visualization in Smart Manufacturing
HKUST
How to alleviate visual clutter and reveal frequent sequences in scheduling?
Cons:
Only reveal sequences following the timeline
Difficult to compare different sequences
Pros:
Reduce visual cluster
Disclose highly concurrent sequences
LiveGantt (Jo et al., 2014) TVCG
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 17: Manufacturing Simulation Visualization
Visualization in Smart Manufacturing
HKUST
How to decrease required simulation ensembles for exploration?
Combine optimization algorithms with visual exploration.
(Matkovic et al., 2014) TVCG
Decrease required simulation runs and guide parameter selection
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 18: Manufacturing Simulation Visualization
Visualization in Smart Manufacturing
HKUST
How to decrease required simulation ensembles for exploration?
Pros:
Reduce the number of data for exploration.
Combine the advantages of both optimization algorithms and human judgment.
Cons:
Does not explain why the result is optimal.
Difficult to compare different parameter configurations for different purposes.
(Matkovic et al., 2014) TVCG
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 19: Manufacturing Simulation Visualization
Visualization in Smart Manufacturing
HKUST
How does the complex production process work?
(Zhou, 2011) Iron & Steel Technology
Visualize the steel manufacturing process.
Volume Rendering +
Augmented Reality (AR)
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 20: Manufacturing Simulation Visualization
Visualization in Smart Manufacturing
HKUST
How does the complex production process work?
Pros:
Immersive environment.
Explain the complex process in a simple and intuitive way.
Cons:
Visual clutter and occlusion.
No visual summary.
(Zhou, 2011) Iron & Steel Technology
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 21: Manufacturing Process Visualization
Visualization in Smart Manufacturing
HKUST
How to detect risks? when does the system need maintenance?
(Wu et al., 2018) PacificVis
Employ advanced algorithms to reveal the risk level of time series data.
Visualization: the stacked bar chart, the pack layout, and the ring map.
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 22: Manufacturing Process Visualization
Visualization in Smart Manufacturing
HKUST
How to detect risks? when does the system need maintenance?
Pros:
Easy to identify sensors in the high risk level.
Guide predictive maintenance.
Cons:
Do not consider the topology of sensors.
Do not verify the correctness of the algorithm.
(Wu et al., 2018) PacificVis
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 23: Manufacturing Process Visualization
Visualization in Smart Manufacturing
HKUST
How to detect risks? when does the system need maintenance?
(Zhou et al., 2018) Journal of Visual Languages & Computing
Heatmap, multi-scale exploration
Adopt a situation awareness model to monitor facilities in a factory producing lithium battery cathode materials.
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 24: Manufacturing Process Visualization
Visualization in Smart Manufacturing
HKUST
How to detect risks? when does the system need maintenance?
Pros:
Intuitive, easy to use
Help non-experts understand and locate problems.
Cons:
Cannot display equipment condition in a long time span.
Scalability: not suitable for a larger system.
(Zhou et al., 2018) Journal of Visual Languages & Computing
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 25: Supply Chain Visualization
Visualization in Smart Manufacturing
HKUST
How to optimize the design of supply chains?
Sourcemap (Bonanni et al., 2010) CHI
Graph-based visualization, incorporate geographic information.
Reveal the transportation path and the carbon footprint.
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 26: Supply Chain Visualization
Visualization in Smart Manufacturing
HKUST
How to optimize the design of supply chains?
Pros:
Supporting visually designing the supply chain network.
Intuitive and easy.
Cons:
Do not consider the uncertainty in demands.
Do not support what-if analysis.
Sourcemap (Bonanni et al., 2010) CHI
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 27: Supply Chain Visualization
Visualization in Smart Manufacturing
HKUST
How to reveal the risk interrelationships between different companies?
(Basole et al., 2014) Decision Support Systems
Visualization: the node-link diagram, the ego-centric network
Interrelationships and risk levels of companies in a three-tier supply chain network.
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 28: Supply Chain Visualization
Visualization in Smart Manufacturing
HKUST
How to reveal the risk interrelationships between different companies?
Pros:
Support subtier network analysis.
Reveal patterns of different risk levels.
Cons:
Only local views.
No geographical information.
(Basole et al., 2014) Decision Support Systems
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 29: Conclusion
Visualization in Smart Manufacturing
HKUST
Visualization in planning and Scheduling
Interactively optimize the planning, the scheduling, and process layouts.
Visualization in manufacturing simulation
Configure parameters, diagnose problems, and understand manufacturing.
Visualization in manufacturing processes
Reveal inefficiencies, anomalies, and bottlenecks; predictive maintenance.
Visualization in supply chain
Visually design the supply chain network; reveal patterns in risks.
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 30: Future Work
Visualization in Smart Manufacturing
HKUST
The uncertainty and multiple constraints of planning are still unresolved.
Reflect uncertainty in demands.
Combine various constraints together.
Predictive maintenance is not fully explored.
Self-monitoring.
Maintenance on demand.
What-if analysis is needed.
What if there is unpredictable fault?
What if there is a increase / decrease in demands / supplies?
The algorithm result is not explained and convincing.
Leverage domain knowledge to understand and build the model.
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 31: Our Approach
Sequence Synopsis: Optimize Visual Summary of Temporal Event Data
System
Evaluation & Summary
HKUST
Notes: First, let me introduce you the background and motivation of visualization in Industry 4.0.

## Slide 32: Sequence Synopsis: Optimize Visual Summary of Temporal Event Data
IEEE Transactions on Visualization and Computer Graphics (TVCG), 2018
Yuanzhe Chen1, Panpan Xu2, Liu Ren2
1Hong Kong University of Science and Technology 2Bosch Research North America
Notes: I am Yuanzhe
This is a joint work with
When I was an intern

## Slide 33: Use Case: Car Faults Analysis
Event Sequences
A
08-20 10:00
Car battery low
B
08-21 12:30 GPS inoperative
C
08-22 12:30
Short circuit
Repair / maintenance
X
t
Car modules like ECUs (electronic control units) / sensors emits fault signals like DTCs (diagnostics trouble codes) during operation.
Fault data is archived for most car brands.
HKUST
Notes: Since we collaborated with analysts from Automotive industry, we also focus on the car faults sequences.
Cars are complex system and contain many modules.
Car modules like…
Nowadays most can brands…
The emitted fault signals forms a sequence of car faults.

## Slide 34: Use Case: Car Faults Analysis
Event Sequences
……
……
t
A
A
A
B
B
B
C
C
C
E
E
D
What are the typical development paths of faults? (Identify sequential patterns )
Do cars matched to the same pattern come from the same country? (correlation analysis)
  Insights support predictive diagnostics (i.e. identify faults likely to happen in the future).
  Better driving experience & warranty cost saving.
HKUST
Notes: When analyzing such sequences, two questions are often asked by the analysts.
First…
Second…
By answering these questions, analysts can get insights to…

## Slide 35: Use Case: Car Faults Analysis
Event Sequences
……
……
t
A
A
A
B
B
B
C
C
C
E
E
D
What are the typical development paths of faults? (Identify sequential patterns )
Do cars matched to the same pattern come from the same country? (correlation analysis)
  Robust to noisy data
  Interpretable results
  Succinct visual overview
HKUST
Notes: When analyzing such sequences, two questions are often asked by the analysts.
First…
Second…
By answering these questions, analysts can get insights to…

## Slide 36: Our approach

## Slide 37: Overview
Our Approach – Sequence Synopsis
Two-part representation of event sequences as lossless compression of the data
Optimal pattern set selection for visual summary based on the Minimum Description Length (MDL) principle
  Optimization algorithm
  Speedup with locality sensitive hashing
HKUST
Notes: In this paper, we propose a novel approach to visually summarize event sequences.
Our method is based on a two part representation of event sequences, where we represent sequences with a set patterns and corrections
Then, based on Minimum Description Length principle, we can select the optimized pattern set to summarize the data.
Then…
I will give more details about the first two points here which tells you what is the proposed visual summary and briefly introduce how we calculate it.

## Slide 38: Two-Part Representation of Event Sequences
Our Approach – Sequence Synopsis
Representative pattern
summarizes multiple sequences.
A
A
A
B
B
B
C
C
C
E
E
D
A
B
C
HKUST
Notes: So what is the two-part representation
Given three cars and their fault sequences, we can identify the common part, which is… we call it the …and intuitively, this pattern can be a summary of these three sequences.

## Slide 39: Two-Part Representation of Event Sequences
Our Approach – Sequence Synopsis
A
A
A
B
B
B
C
C
C
E
E
D
A
B
C
Corrections - event insertions (edits) recover the original sequences from the pattern.
  Use sequential patterns for visual summary.
  Model information loss with the required edits (corrections).
Representative pattern
summarizes multiple sequences.
HKUST
Notes: Then to recover the sequences with the pattern , the inserted events are defined as corrections, or edits.
So pattern and corrections is the two-part representation of event sequences.
We can use sequential patterns…

## Slide 40: Two-Part Representation of Event Sequences
B
A
Our Approach – Sequence Synopsis
A
A
B
B
C
C
C
E
E
D
A
B
C
Event deletion is another possible type of edit.
Representative pattern
summarizes multiple sequences.
  Different types of edits allow different variations from the pattern. Enable noise tolerant & robust pattern matching.
HKUST
Notes: Besides inserting events, we can also allow recovering the sequences from pattern by delete certain events, like…
So different types of… We can also define other type of edits besides insertion and deletion. The ability to generalize the edits makes…

## Slide 41: Two-Part Representation of Event Sequences
Our Approach – Sequence Synopsis
What can be considered as a good set of patterns to summarize a collection of event sequences?
Patterns
Edits (Corrections)
Event Sequences
=
+
HKUST
Notes: This figure shows a more generic example. Here we summarize … into two patterns.
Whether this is a good summary or not? Why not summarize…
Here we need to define what is a god set of patterns for visual summary.
The basic observation is that we want both small number of patterns and edits. Because…

## Slide 42: The Minimum Description Length (MDL) Principle
Our Approach – Sequence Synopsis
L = L(M) + L(D|M)
Model description length
Data description length with the help of the model
Widely used information-theoretic criteria for model selection
Introduced by Jorma Rissanen in 1978
Formalizes “Occam’s Razor”
“We consider it a good principle to explain the phenomena by the simplest hypothesis [model] possible.” (but not simpler)
- Ptolemy (c. AD 90 – c. AD 168)
The best model (or hypothesis) of a data set should minimize its total description length:
HKUST
Notes: To find an optimized pattern set, we apply
MDL principle is widely used…originated from occam’s razor
It states that the best model is the simplest model, that is the model minimize total cost
And the cost consists of two part,…, which perfect fit with the observation I just mentioned.

## Slide 43: Description Length of Event Sequences
Our Approach – Sequence Synopsis
7
6
Trade-off between reducing visual complexity & minimizing information loss.
L = L(M) + L(D|M)
sum(lengths of patterns)
# min edits (corrections)
HKUST
Notes: Apply MDL to our problem, the model description length corresponds to …and the data description length corresponds to …
The last term… you can Refer to our paper for more detail.
According to MDL principle, we need find the pattern set which can minimize the total cost.
And the remark here is…since we want to visually summarize the data with patterns, the MDL finds the trade-off…

## Slide 44: Optimize Description Length for the Best Set of Patterns
Our Approach – Sequence Synopsis
Basic Idea: iteratively find & merge two groups of sequences with maximum description length reduction
How to calculate description length reduction?
  Find representative sequence for the merged group
  Calculate the minimum number of edits (insertion, deletion, swapping event positions) needed to transform the representative sequence to the individual sequence in the merged group
    Assuming insertion & deletion are allowed. Longest common subsequence (LCS) algorithm can be applied to calculate min #edits
  Sum up the description length
HKUST

## Slide 45: Optimize Description Length for Best Set of Patterns
Our Approach – Sequence Synopsis
Basic Idea: iteratively find & merge two groups of sequences with maximum description length reduction
…
-5
-4
HKUST
Notes: The basic idea…
In this example, in the beginning,…we go through each pair of sequences and try to merge them as one pattern
Then we choose…and merged them as a new pattern
Keep doing this until no further reduction is possible

## Slide 46: Algorithm Speedup through Locality Sensitive Hashing (LSH)
Our Approach – Sequence Synopsis
Bottleneck of the approach: find best pair of event sequence groups to merge
Locality sensitive hashing: algorithm for fast approximate neighbor search
HKUST
Notes: To support interactive analysis, we further speed up…
In this example, each dot represents one sequence

## Slide 47: Algorithm Speedup through Locality Sensitive Hashing (LSH)
Our Approach – Sequence Synopsis
Bottleneck of the “vanilla” approach: find best pair of event sequence groups to merge
Locality sensitive hashing: algorithm for fast approximate neighbor search
20x ~ 50x speed gain with LSH compared with "vanilla" approach
HKUST
Notes: To support interactive analysis, we further speed up…

## Slide 48: Advantages
Our Approach – Sequence Synopsis
Simultaneous event sequence clustering and pattern extraction
Soft constraints on pattern matching, therefore robust to noisy data
Generalizability: possibility to include different sequence editing operations (e.g. event insertion, deletion, swapping positions)
HKUST
Notes: To summarize, …

## Slide 49: System

## Slide 50: Visual Design
System
Corrections
Patterns
Original Data
Visual Design
HKUST
Notes: Each pattern -> sequence
Height of the rectangle -> how many events match with the pattern -> missing events E
Triangle -> insertion
Larger triangle -> more insertion

## Slide 51: Architecture
System
HKUST
Notes: We also built an visualization system to support interactive analysis. Here is the system architecture.

## Slide 52: Supportive Views, UI, Case Study – Vehicle Fault Analysis
System
HKUST

## Slide 53: Case Study – Application Log Analysis
System
Dataset:
  D. Fisher. Agavue event data sample
Size:
  ~2000 user sessions
Description:
  Interaction log of using a data visualization application
HKUST
Notes: We also applied our method to application log analysis.
Here we use a public dataset contains 2000 user sessions.
Each session records the actions when a user interact with the application to generate visualization like bar chart or treemap.
A… B…less variation

## Slide 54: Evaluation & Summary

## Slide 55: Comparative Experiment
Evaluation & Summary
Dataset: Vehicle Faults
Left: EventFlow
Right: Sequence Synopsis
HKUST
Notes: Emphasize that our approach is noise tolerant

## Slide 56: Contributions
Evaluation & Summary
A new application domain of event sequence visualization
A generic two-part representation of event sequences that:
  Quantifies visual complexity & information loss in visual summaries
  Combined with the MDL principle, defines an optimal set of patterns for summary
An efficient algorithm to optimize visual summary using LSH
A visual analytics system that supports interactive analysis of real-world event sequences from different application domains
HKUST

## Slide 57: Future Work
Evaluation & Summary
Revise model representation to discover multiple patterns in a single sequence
Towards quantifiable visual designs by applying the MDL principle to different types of data: graph/networks, time series …
HKUST

## Slide 58: Introduction
ViDX: Visual Diagnostics of Assembly Line Performance in Smart Factories
The ViDX System
Summary
HKUST
Notes: First, let me introduce you the background and motivation of visualization in Industry 4.0.

## Slide 59: Panpan Xu et al.
Best Paper Honorable Mention
IEEE VAST, Oct 2016
ViDX: Visual Diagnostics of Assembly Line Performance in Smart Factories

## Slide 60: Smart factories in Industry 4.0
Introduction
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
60
*Image source: http://www.alamy.com/stock-photo/19th-century-factory.html
Factories in the 19th century*.
Manufacturing today.
Towards Industry 4.0 (a.k.a. connected industry, industrial internet)
Digitalized
Automated
Connected
Notes: Manufacturing today is very different from the past.
Today we are in the middle of a evolution where the factories are becoming digitalized, automated, connected and increasingly smart
People call it the industry 4.0 , or … in different countries

## Slide 61: Big data in smart factories
Introduction
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
Sensors
Programmable
Logic
Controllers
Data stream
Status
Monitoring
Predictive Maintenance
Process Optimization
Performance
Troubleshooting
Visual
Analytics
temperature,
humidity, pressure, …
cycle time,
progress, error, …
RFID*
location tracking info, …
* RFID: Radio frequency identification
Data-driven decision making
61
Notes: But exactly how can factories be smart?
In the past years, people have installed a lot of sensors & digital controlling device to the ..
They collect a lot of data,
Transform the data into insights to support status monitoring,
How to do it?
visual analytics can play a very important role here

## Slide 62: Challenges of real manufacturing data
Introduction
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
High volume & speed
  Short cycle time (time to finish one step)
  High throughput
High complexity
  Tens to hundreds of measurements along a single manufacturing line
62
Notes: Challenges of real manufacturing data
Visualization can give a transparent overview of the complex and large manufacturing data

## Slide 63: Our work
Raise the awareness of this new, important and exciting research area for visual analytics
ViDX: The first visual analytics system for real manufacturing data in industry 4.0 applications.
  Data provided by Bosch Anderson plant at South Carolina producing hydraulic modules, electronic modules and sensor elements in cars (deployment in progress)
Addressing challenges with novel visualization & interaction
  Target user: shop floor technicians/operators and managers
  Application: intuitive status monitoring & easy performance troubleshooting on assembly lines
  Data: complex, large scale manufacturing process data.
Introduction
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
63
Notes: We take on real data set from a manufacturing plant capturing their operation histories .
And introduce …

## Slide 64: Data
The ViDX System
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
Work Station S1
Work Station S2
Work Station S3
Parts/Products A, B, C …
Data:
  When a part/product arrives at which station (with the derived cycle time)
  Which fault occurred
12:00:03 Oct 28
12:00:58 …
Fault occured
12:01:08 …
Cycle Time
64
Notes: The first step
what kind of data?
Data come from assembly line
A typical assembly line is composed of a sequence of work stations
the part goes through different stations to be processed and assembled to form the final product
Modern manufacturing lines controlled by programmable logic controller can trace when each product arrive at which station, and also record the error occurred in the process.

## Slide 65: Data
The ViDX System
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
Database for historical records
(millions per year for a single production line).
65
Notes: A record For each and every one of the products about its history

## Slide 66: Tasks & system requirements
The ViDX System
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
Task: performance troubleshooting
  Identify when (during which minute/hour/day…), where (on which work station), how production efficiency decreases.
  Determine the effect of faults on production efficiency.
Work Station S1
Work Station S2
Work Station S3
Parts A, B, C …
12:00:03 Oct 28
12:00:58 …
12:01:08 …
System requirements
  Scalable to handle year long records.
  Support both historical data analysis & real-time monitoring.
66
Notes: The data is just sitting in the database and but it actually has the potential to support the
Why real time monitoring?

## Slide 67: Inspiration: E.J. Marey’s graphical train schedule from 1880’s
The ViDX System
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
Train
Stations
Timeline
67
Notes: Our visual design is inspired by …, you can also find this graph in tufte’s book
thus, the slope of the line reflects the speed of the train: the steeper the line, the faster the train.
http://marlenacompton.com/?p=103

## Slide 68: Idea 1: Visualize manufacturing processes as Marey’s Graph
The ViDX System
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
00:00
00:10
00:20
00:30
00:40
00:50
00:00
00:10
00:20
00:30
00:40
00:50
00:02
00:06
00:08
00:13
00:16
00:30
00:35
00:37
Outlier process:
delayed at station S3’.
S1
S2
S3’
S4
S5
S6
S9
S10
S3
S7
S8
Work
Stations
enter
leave
68
Notes: This is the manufacturing data visualized as marey’s graph
Instead of train stations, we now have …
Instead of trains, we have products

## Slide 69: Intuitive visual patterns for performance troubleshooting
The ViDX System
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
☑Normal, efficient operation
☒The assembly line stopped
☒Processes stuck at some station
69
Notes: When we plot the real data, more visual patterns emerge,
Rhythmic pace
station s1 and s2 stopped processing, waiting for s3 to
finish handling the parts whose processing have been delayed

## Slide 70: How to scale-up? (related work)
The ViDX System
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
Visualize public transportation schedules [Palomo et al. 2015]
Kernel density estimation (KDE)
Outliers blurred out.
70
Notes: Outliers hidden in visual clutters
One way to do
But the problem here is that kernel density estimation tends to blurr out the outliers

## Slide 71: Idea 2: Interactive outlier detection and visualization.
The ViDX System
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
Outlier-preserving visual aggregation.
Aggregate normal processes.
Keep outliers.
How to define the outliers?
Two interactive outlier detection techniques:
Samples brush
Quantiles brush
71
Notes: We propose a different approach

## Slide 72: Animated radial graph for real-time production progress monitoring
The ViDX System
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
Original design proposed by the target user.
Redesigned graph.
72
Notes: three layers of concentric rotating circles. The inner
circle completes one cycle when a product finishes its procedures on one
station. The circle in the middle completes one cycle when the product
finishes its procedures on the entire assembly line. The outer circle completes
one cycle for an eight hour work shift. A slower rotation speed of
the inner circle means longer cycle time on a station.

## Slide 73: User interview
The ViDX System
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
Participants
  11 users, all have experience with basic visualization techniques (e.g., barcharts)
Summary of feedback
  Samples brush is preferred over quantiles brush for its intuitiveness.
  Extensions suggested to apply the current system for analyzing other process related parameters.
  Deployment of the system in progress
“This is a good interface for gaining an intuitive picture of how the line is running. These same methods could applied to process parameters during the manufacture of parts giving engineers the intuitive picture of process stability”.
“it’s very effective in the system’s ability to show real-time data [in the radial graph] and highlight abnormalities”
73

## Slide 74: Contributions
The first visual analytics system for real data in Industry 4.0 applications.
Application & extension of the Marey’s graph to visualize large amount of manufacturing processes with outlier-preserving visual aggregation techniques.
Two novel interactive outlier detection techniques:
  Samples brush based on label propagation algorithms
  Quantiles brush based on statistical summaries
Summary
Research and Technology Center North America | CR/RTC1.4-NA | 8/21/2016
© 2016 Robert Bosch LLC and affiliates. All rights reserved.
74
Notes: To summarize

## Slide 75
Thank You!
Dong SUN
dong.sun@connect.ust.hk
https://www.cse.ust.hk/~dsunae/